## Slide 1: The Cost of Fixing Hold Time Violations in Sub-threshold Circuits Yanqing Zhang, Benton Calhoun University of Virginia
Motivation and Background
Power
Performance
High end, decrease
VDD for lower power
Low end, sub-threshold for increased lifetime
Hold time important!
  Shift register structures in computer architecture, e.g. re-order buffer, result bus reservation, etc.
  Test structures, e.g. scan chains
Much more problematic in sub-threshold
  More susceptible to effects of process variations
  Long variation distribution tail
  Effects clock skew, slew, and logic delay
  Largely un-correlated  higher chance of failure!
Conventional methods adequate?
  Improving clock network costs power/energy
  Excessive hold buffer insertion costly
  Could undermine purpose of low power
tSKEW
Excessive buffer
insertion is COSTLY
Clock network
optimization is COSTLY
Near- or sub-threshold circuits vital for low power
  Power wall imminent for high end applications
  Battery life/form factor constraint for low end
New design problems in sub-threshold
  Performance degradation
  More susceptible to process variation
  Smaller Ion/Ioff –less noise tolerance
  Different timing characteristics
      Hold time one problem
Thus, need to analyze new design space
  How to adapt to sub-threshold?
  How to design in sub-threshold?
  Other alternative methods needed?
Tool Flow and Simulation Test Setup
45 nm PTM standard cell library used
  High Vt for low power
  TT corner
  Vt only variation (Gaussian distribution)
Library characterization @operating condition
  In contrast to characterization @ nominal VDD and then scaling VDD down
  Characterized @ VDD = 0.35 V
  Captures sub-threshold delays
  Nominal margins
Standard synthesis flow
  Synthesis, Place and Route
  Power aware clock design
  Simplified delay model for simulation, wire RCs not accounted
Standard Cell Library
Cells.lib
Timing_arc:
Delay_value
@ VDD = 0.35 V
Library Characterization
Synthesis, Place and Route
Monte-Carlo hold time simulations
  128 stage shift register as design under test
  Each design case subject to 100 iterations
    Simulation time considerations
Sweep amount of buffer insertion
  Hold constraint slowly increased
  Place and route tool performs timing closure
  Buffer penalty measured as power overhead needed to shift data from input to output of shift register
Sweep design of clock network
  Both slew and skew are design variables
  Clock tree synthesis also done by EDA tool
  Clock overhead measured as power needed to shift data from input to output of shift register
......
......
128 stages total
Sweep buffer insertion
Sweep slew
Sweep skew
In
Out
?
Power breakdown:
Preg =Register power
Pclk =Clock network power
Phold =Hold buffer power
Sub-threshold
Effects of Process Variation on Cell Delay in Sub-threshold
Count (% Total)
Cell Delay
25
20
15
10
5
0
µ-2σ
µ-σ
µ
µ+σ
µ+2σ
µ+3σ
Concluding Remarks
Conclusions:
  Slew is least effective variable for hold fixing
  For certain register load, use smaller clock trees
  Hold buffer insertion is expensive (>50% total!)
  Yield requirements may compromise low power
  Complex clock trees fail miserably
Other solutions worth looking into?
  Conventional methods scaling in sub-threshold is worrisome
  Larger designs mean inheritently complex clock trees skew is a major player
  Buffer insertion solution proven as great overhead need other methods
  Better place and route algorithms?
  Delay cell design?
  Timing scheme ‘tricks’?
Results: Effects of Skew
Test setup:
  Iso-slew at register
  Same amount of buffer insertion
  Constant level (4) of clock tree
  # of clock tree branches (skew) swept
Observations
  Skew is a major factor
  Yields very low for skews > 2 clock buffer delays
  Process variation culprit in undermining clock path balancing
  Tendency is more levels of clock tree = worse skew (NOT more balancing)!
Yield (%)
80
70
60
50
40
Skew Effects on Yield
Max Skew (# of clock buffer delays)
1
2
3
4
Results: Effects of Slew
Test setup:
  2 level, 4 branch clock tree used (drive sufficient)
  Iso-skew with similar clock topology
  800ns clock slew @ clock input
  Case 1: max allowed clock buffer swept(8X,16X,32X…), no hold buffer insertion
  Case2: min clock buffer (8X), hold buffer insertion
Observations
  Slew not the most effective hold time solution
  Little changes in yield for improving slew
  Clock energy becomes expensive
  For same power budget, (smaller clock tree+buffer insertion) > (bigger clock tree, no buffer insertion)
Case 1 vs. Case 2
Pclk
Preg
Phold
Normalized Power Consumptions
1
0
2
3
4
68
81
Yield (%)
32X clock tree,
No buffers
8X clock tree,
Hold buffers
Slew Affects on Yield
Pclk
Preg
Relative Power Consumptions
Yield (%)
70
60
50
45
40
55
65
Slew (ns)
10
14
18
22
26
8X
16X
32X
Results: Cost of Buffer Insertion
Test setup:
  Simple 2 level, 4 branch clock tree used (drive sufficient)
  Minimizes skew (1 clock buffer delay)
  Optimum clock slew @ clock input
Observations
  Buffers VERY expensive (>50% total power)
  Different size buffers used, data slew a factor
  Small buffers add logic delay
  Large buffers improve data slew
  Steep penalty as yield increases
Pclk
Preg
Phold
Cost of Buffer Insertion in Hold-time Fix
% Power Overhead of Buffers
Yield (%)
Total Circuit Power (Normalized)
40
50
60
70
80
90
100
0
70
60
50
40
30
20
10
1
2
3
96
97